## Slide 1: SWOT Tank Water Tracker for Sri Lanka
IS4990 COMPREHENSIVE GROUP PROJECT · PROJECT PROPOSAL
An AI system that estimates how much water each tank holds, using free satellite data
Group 6 · JARVIS
Supervisors: Dr. Upeksha Ganegoda (IT) · Prof. (Mrs) Thanuja Sandanayake (IDS)
October 2026
Tanks around Mahakanadarawa, Sentinel-2, 28 Feb 2026. Contains modified Copernicus Sentinel data 2026.

## Slide 2: We can see the tanks, but not the water in them
~23,000
small tanks of 80 ha or less in Sri Lanka, the base of dry-zone farming
National Tanks Survey, in Lopane et al., 2025
118
reservoirs publish daily water levels; village tanks publish none
Irrigation Department daily sheet, 25 Oct 2026
10,650
water bodies mapped from satellites, but by area only, with no volume
IFAD, 2026
A shallow tank and a deep tank of the same size hold very different amounts of water.
432 tanks of 6.25 ha or more in our study area (blue)
Sentinel-2, 28 Feb 2026 · outlines © OpenStreetMap contributors

## Slide 3: SWOT gives the height. We turn it into water
What SWOT gives
The water height of each lake, about twice every 21 days
Only for lakes in its prior lake list
Mostly "suspect" readings on small village tanks
No volume, and nothing between passes
What our project adds
Water area from Sentinel-1 and Sentinel-2 by AI, even under cloud and water plants
A height–area–volume curve for every tank
Storage in m³ and % full, every 5–12 days
Accuracy checked against Irrigation Department gauges
A dashboard for irrigation officers and farmers
SWOT is the ruler. We turn its readings into water in the tank.

## Slide 4: SWOT: a satellite that measures water height
Illustration: NASA/JPL-Caltech
Dec 2022
launched by NASA and CNES (France)
120 km
wide strip measured on each pass
21 days
until the same pass comes back
2 passes
see our tanks: 273 and 092

## Slide 5: What SWOT sees: one pass, every lake at once
198
lakes measured in a single pass
SWOT pass 273 on 11 Oct 2026, in our 44 × 55 km study area
Each colour is the water height SWOT measured, in metres above sea level.
All 5 of our reservoirs were measured on this pass, for example Hurulu Wewa at 127.91 m.
SWOT cannot measure the strip right under itself, shown hatched on the map.
Data: NASA/JPL and CNES, SWOT Lake Single-Pass product, version D, from NASA PO.DAAC.

## Slide 6: Clouds hide the tanks. Radar sees through them
Sentinel-2, clear day
Hurulu Wewa, 28 Feb 2026 · optical, 10 m
Sentinel-2, monsoon cloud
Hurulu Wewa, 30 Nov 2025 · the tank is hidden
Sentinel-1 radar
Hurulu Wewa, 2 Dec 2025 · water shows dark
Only 17–22% of Sentinel-2 dates were clear over our test tanks, so radar is a core input.
Contains modified Copernicus Sentinel data 2025–2026.

## Slide 7: Study area: 5 reservoirs and 8 village tanks
5 major reservoirs
Hurulu Wewa, Mahakanadarawa, Manankattiya, Nachchaduwa and Nuwara Wewa, all with daily gauge readings
8 village tanks
0.4–5 km from Mahakanadarawa: 2 open water, 3 mixed and 3 mostly covered by water plants
Seen by SWOT passes 273 and 092
All 13 tanks, about twice every 21 days, with 47–90 usable readings each since July 2023
Why here
Dry-zone tank cascades (ellanga), flat land, and official gauges to check against

## Slide 8: How it works
Sentinel-1 and Sentinel-2
Radar and optical images, every 5–12 days
AI water map
Open water, water under plants, and land
SWOT water heights
From NASA's Hydrocron service since July 2023, with poor readings removed
Height–area–volume curve
One per tank: each SWOT height paired with the AI water area of the same day
Storage every
5–12 days
Each new water map becomes a volume, shown on a dashboard
Checked against Irrigation Department gauges and official storage figures

## Slide 9: Our method in three pictures: Hurulu Wewa
Low
127.59 m SWOT height
6.1 km² of water
Sentinel-2 29 Jul 2023 · SWOT 30 Jul 2023
Half full
129.50 m SWOT height
8.3 km² of water
Sentinel-2 and SWOT, 30 Jul 2025
Full
132.35 m SWOT height
10.8 km² of water
Sentinel-2 28 Feb 2026 · SWOT 10 Mar 2026

## Slide 10: Three years of SWOT water levels
Monthly average of best-quality readings, in metres above each reservoir's lowest month.
Chart: Hurulu Wewa
| 2023 | 2024 | 2025 | 2026
Hurulu Wewa | 1.64 | 2.74 | 4.73 | 4.81 | 4.25 | 3.09 | 2.43 | 1.73 | 0.52 | 0.25 | 0.03 | 0.15 | 2.83 | 4.84 | 4.72 | 4.92 | 4.02 | 4.5 | 3.36 | 1.82 | 1.31 | 1.23 | 1.23 | 0.4 | 5 | 4.72 | 4.3 | 4.42 | 3.32 | 3.67 | 2.26 | 0.84 | 0.16 | 0.06 | 0
71 best-quality readings
rose and fell up to 5.0 m
Chart: Mahakanadarawa
| 2023 | 2024 | 2025 | 2026
Mahakanadarawa | 0.69 | 3.95 | 4.39 | 3.93 | 3.26 | 2.41 | 2.07 | 1.72 | 0.8 | 0.57 | 0.45 | 0.31 | 3.74 | 4.35 | 4.34 | 4.38 | 2.7 | 2.1 | 1.88 | 0.4 | 0 | 4.2 | 4.09 | 4.2 | 4.11 | 3 | 3.46 | 2.97 | 2.34 | 1.99 | 1.77 | 1.59
63 best-quality readings
rose and fell up to 4.4 m
Chart: Manankattiya
| 2023 | 2024 | 2025 | 2026
Manankattiya | 3.43 | 3.45 | 3.45 | 3.31 | 2.84 | 2.27 | 1.86 | 1.38 | 0.84 | 0.8 | 0.89 | 0.95 | 1.37 | 3.66 | 3.48 | 2.67 | 2.21 | 1.85 | 1.72 | 1.5 | 1.17 | 3.25 | 3.09 | 2.76 | 2.63 | 1.93 | 1.89 | 1 | 0.59 | 0
57 best-quality readings
rose and fell up to 3.7 m
Chart: Nachchaduwa
| 2023 | 2024 | 2025 | 2026
Nachchaduwa | 0 | 2.47 | 2.85 | 2.75 | 2.55 | 2.39 | 1.79 | 1.53 | 1.93 | 1.18 | 1.06 | 1.67 | 1.62 | 2.78 | 2.86 | 2.75 | 2.96 | 2.61 | 2.25 | 1.44 | 0.84 | 0.78 | 1.79 | 2.4 | 2.58 | 2.39 | 2.6 | 1.81 | 1.25 | 0.15 | 0.08 | 0.38
55 best-quality readings
rose and fell up to 3.0 m
Chart: Nuwara Wewa
| 2023 | 2024 | 2025 | 2026
Nuwara Wewa | 0 | 3.99 | 4.28 | 3.72 | 3.64 | 3.04 | 2.43 | 2.97 | 2.38 | 1.98 | 1.8 | 1.09 | 3.86 | 4.33 | 4.05 | 4.15 | 3.95 | 3.38 | 2.99 | 2.4 | 2.12 | 2.01 | 4.28 | 3.71 | 3.53 | 3.18 | 3.12 | 3.25 | 2.84 | 2.28 | 2.07 | 2.02
53 best-quality readings
rose and fell up to 4.3 m
Source: NASA PO.DAAC Hydrocron, SWOT lake product version D, July 2023 to October 2026. Gaps are months without a best-quality reading.

## Slide 11: We tested the data before proposing
Five quick checks in October 2026, using the real SWOT, Sentinel-2 and gauge data.
1 · LAKE IDS
86%
of Irrigation Department tanks in our area have a SWOT lake ID (43 of 50); 58% of all mapped tanks
RISK
2 · HEIGHTS
26,641
SWOT readings on 400 lakes since July 2023; village tanks get mostly "suspect" readings
RISK
3 · GAUGE CHECK
~1 m
difference between SWOT and gauges on 4 reservoirs, with readings 13 to 20 days apart
OK
4 · WATER AREA
17–22%
of Sentinel-2 dates clear; water plants hide the water in 3 village tanks
RISK
5 · TRAINING DATA
2
labelled water datasets ready to use: Sen1Floods11 and S1S2‑Water
PASS
Verdict: GO, with changes. Sentinel-1 radar and a water-plant class became core parts of the plan, and RQ2 now tests SWOT's "suspect" readings.

## Slide 12: Why these tanks? We checked all of Sri Lanka
6th of 187
Hurulu Wewa's rank among Sri Lanka's big lakes (1 km² or more), by best-quality SWOT readings
All 5 of ours are in the island's top 22, and they are the top 5 in our study area
The island's top tanks are spread from Puttalam to Hambantota, far from our village tanks
Ours sit next to the 8 village tanks and share the same 2 SWOT passes
All 5 have daily Irrigation Department gauges; 2 of the island's top 5 tanks do not
Best quality: quality flag 0, crossover flag 0–1, dark water 10% or less (Köhn and Nielsen, 2026).

## Slide 13: Research questions
1
How accurately can deep learning map tank water from Sentinel-1 and Sentinel-2, even under cloud or water plants?
Measured by IoU and F1 against hand-labelled water masks
2
How accurate is SWOT on reservoirs and on small village tanks, and can its "suspect" readings be trusted?
Measured by error in cm against gauge readings
3
Does AI water area plus SWOT height give storage close to official and measured values?
Measured by error as a % of capacity
4
Can storage be forecast 2–4 weeks ahead from recent storage and rainfall?
Stretch goal, compared with a "no change" forecast

## Slide 14: What we will deliver, and when
A labelled dataset of Sri Lankan tank water masks
An AI water map that works under cloud and water plants
Height–area–volume curves for all 13 tanks
Storage every 5–12 days, shown on a dashboard
A research paper, for example for UoM's ICITR conference
Nov 2026
Proposal, ethics and data requests
15 Dec 2026
Study area confirmed after the cascade and name checks
Dec 2026 – Apr 2027
Labelled data, gauge readings, AI water model and SWOT curves
Mar – May 2027
Storage estimates, validation and dashboard
30 Jun 2027
Thesis, paper and final submission

## Slide 15: Thank you
Questions and feedback are welcome.
Data sources
SWOT: NASA/JPL and CNES, Lake Single-Pass product version D (PO.DAAC, Hydrocron)
Sentinel-1 and Sentinel-2: ESA Copernicus (Earth Search and Microsoft Planetary Computer)
Reservoir levels and outlines: Irrigation Department of Sri Lanka
Tank outlines © OpenStreetMap contributors; Sri Lanka boundary: geoBoundaries
SWOT illustration: NASA/JPL-Caltech
See SWOT readings for any lake:
SWOT Lake and River Explorer